## Slide 1: Electronic Devices
Lab Lecture 1
This document might contain some excerpts and pictures from various books and other sources. The author doesn’t claim any rights to the topics discussed in this video. This topics has been presented in a way to help out students in BRAC university, Bangladesh

## Slide 2: Diode Logic Gates

## Slide 3: Diode Logic Gates

## Slide 4: Diode Logic Gates
Diode logic means construction of Boolean logic gates from diodes
Figure : Diode logic OR gate
IF both inputs and are zero(0) , then both diodes will be off and the output will be low
If either of the input is high , then corresponding diode will turn on which will raise the output to high.
Same case when both inputs are high.

## Slide 5: Diode Logic Gates
Figure : Diode logic OR gate
Input A | Input B | Output Y
0 | 0 | Low
0 | 5(High) | High
5(High) | 0 | High
5(High) | 5(High) | High

## Slide 6: Diode Logic Gates
Figure : Diode logic AND gate
IF both inputs and are zero(0) , then both diodes will be on and the output will be low
If either of the input is high , then corresponding diode will turn off but the other diode will be on. For this output will be low
When both inputs are high no diode will conduct. For this no current will pass through the diodes and output will be clamped high.

## Slide 7: Diode Logic Gates
Figure : Diode logic AND gate
Input A | Input B | Output Y
0 | 0 | Low
0 | 5(High) | Low
5(High) | 0 | Low
5(High) | 5(High) | High

## Slide 8: Diode Logic Gates
Figure : Diode logic INVERTER
When the input is HIGH, the transistor will turn on. Both junctions of the transistor will be forward biased, as a result it will be in saturation mode. In saturation mode, the voltage between emitter and collector is close to 0 volt (~0.1 V) . So , output will be LOW when the input s high.
When the input is LOW , the transistor will be in cutoff mode ( because no current will be passing through the base) . So output will be HIGH.

## Slide 9: Diode Logic Gates
Figure : Diode logic INVERTER gate
Input | Output Y
LOW | HIGH
HIGH | LOW

## Slide 10: Simulation
Figure: Schematic of DL OR gate

## Slide 11: Simulation
Figure: Schematic of DL AND gate

## Slide 12: Simulation
Figure: Schematic of DL INVERTER gate